## Slide 1: Cryptography

## Slide 2: Why Cryptography?

## Slide 3
BRUCE
STARK
https://www.youtube.com/watch?v=MK0SrxBC1xs

## Slide 4: Reasons for using Cryptography
Integrity
Authenticity
Confidentiality.

## Slide 5: Algorithms suggested by AUTOSAR
Hashing Functions : A Hash function is a algorithm that takes an arbitrary amount of data input and produces a fixed size output of enciphered text called a hash value.
1. SHA-1
2. SHA-2
* Length: 256, 384 and 512 bits
3. SHA-3
* Length: 256, 384 and 512 bits
SHA 256

## Slide 6: Algorithms suggested by AUTOSAR
2. Symmetric Ciphers : A Symmetric cipher is one that uses same key for encryption and decryption.
1. AES
* Key Length: 128, 192 and 256 bits
2. Camellia
* Key Length: 128, 192 and 256 bits
3. ChaCha20

## Slide 7: Algorithms suggested by AUTOSAR
3. Asymmetric Encryption/Decryption and Signature Handling : Asymmetric cipher is the one which use two different keys to encrypt and decrypt the data.
1. RSA
* Key Length: 2048, 3072 and 4096 bits
* Padding: PKCS#1 v2.2
2. Curve25519/Ed25519
3. NIST curves P256, P384 and P521 / ECDSA
Private Key
Public Key

## Slide 8: Algorithms suggested by AUTOSAR
4. Message Authentication Code (MAC) : MAC Algorithm is a symmetric key cryptographic technique to provide message authentication. For establishing MAC process, the sender and receiver share a symmetric key K.
1. CBC – MAC
2. CMAC
3. GMAC
4. HMAC

## Slide 9: Algorithms suggested by AUTOSAR
5. Random Number Generation : A Random number generator is a mathematical construct, either computational or a hardware device that is designed to generate a random set of numbers.
1. Deterministic Random Number Generator(DRNG)
2. True Random Number Generator(TRNG)

## Slide 10: Certificates handling
5. Certificates : A Public key certificate is a digitally signed document that serves to validate the sender’s authorization and name.
The certificate consists of a specially formatted block of data that contains name of the certificate holder and holder’s public key as well as the digital signature.
1. User Certificate
2. Intermediate Certificate
3. Root Certificate
X.509 Ref : https://en.wikipedia.org/wiki/X.509

## Slide 11: Cybersecurity Mechanism Variants:
1. Software Based
2. Hardware Based

## Slide 12: Secure Flashing:
Software Package
Hashing
(SHA 256)
Encryption
(RSA 2048)
Private Key
Software Package
Encrypted Hash
Software Package Signing with Private Key
Software Package Verification using Public key
Software Package
Encrypted Hash
Hashing
(SHA 256)
Decryption
(RSA 2048)
Public Key
If Hash Value is Equal – Verification Passed
Else if Hash Value is Not Equal – Verification Failed
Hashing
(SHA 256)

## Slide 13: Secure Flashing: Certificate Usage : Variant 1
Software Package
Hashing
(SHA 256)
Encryption
(RSA 2048)
Private Key
Software Package
Encrypted Hash
Software Package Signing with Private Key
Software Package
Encrypted Hash
Hashing
(SHA 256)
Decryption
(RSA 2048)
Public Key
If Hash Value is Equal – Verification Passed
Else if Hash Value is Not Equal – Verification Failed
User Certificate.
User Certificate.
User Certificate Verification
If User Certificate Verification Passed
Software Package Verification using Public key
Hashing
(SHA 256)

## Slide 14: Secure Flashing: Certificate Usage : Variant 2
Software Package
Hashing
(SHA 256)
Encryption
(RSA 2048)
Private Key
Software Package
Encrypted Hash
Software Package Signing with Private Key
Software Package
Encrypted Hash
Hashing
(SHA 256)
Decryption
(RSA 2048)
Issuer Public Key
If Hash Value is Equal – Verification Passed
Else if Hash Value is Not Equal – Verification Failed
CertStore.
Certstore COT Verification
If Certstore COT Verification Passed
Software Package Verification using Public key
Hashing
(SHA 256)

## Slide 15: AUTOSAR Adaptive Platform Cryptography

## Slide 16: Agenda
© ZF Friedrichshafen AG
2.
3.
4.
5.
6.
1.
7.
8.
12.
11.
10.
9.
Overview – Crypto Stack
Overview – Reference Architecture
Overview – Crypto Service Manager
Overview – Crypto Driver
Supported Features – Crypto Stack
API Overview – TBD..

## Slide 17: Overview – Crypto Stack
          Functional Cluster which is responsible for construction and supervision of cryptographic primitives and offers interfaces to Adaptive Applications.
          Provides multiple implementations of cryptographic algorithms, key management, dynamic generation of key, etc.
          Provides key storage - keys may be stored internally in the crypto backend (Crypto Driver) or
          externally and imported/exported on demand.
          Supports both hardware and software implementation of cryptographic primitives
          (selectable during runtime).
          Protection of keys and key usage can be provided by constraining keys to particular usages
          (e.g. decrypt-only).
          Limitation of the availability of keys to individual applications as reported by IAM.

## Slide 18: Overview – Reference Architecture
          AUTOSAR AP only defines the high-level Crypto Stack API exposed to applications.
          The API is designed to support encapsulation of security-sensitive operations and decisions in a separate component, such as a Hardware Security Module (HSM).
          The API can also be used to protect session keys and intermediate secrets when processing cryptographic protocols such as TLS and SecOC.

## Slide 19: Overview – Crypto Service Manager
          Implements platform-level tasks consistently across applications
          (access control, certificate storage, etc.)
          Coordinates the offloading of functionality to a Crypto Driver (Library/HSM)

## Slide 20: Overview – Crypto Driver
          Can be software library or hardware (HSM)
          When both are available, selection is done during run-time
          Typically complete set of key management and crypto functions are implemented to accelerate crypto operations and protect managed keys from malicious applications
          (permission needs to be granted for operations)

## Slide 21: Supported Features – Crypto Stack
          Symmetric and asymmetric encryption and decryption.
          Hash algorithms (to identify data manipulation).
          Generation, importing, and storing of public/private keys in a secured manner.
          Random number generation
          Support of PKI systems (incl. CSR and CRT)
           X.509 certificats
           PKCS#7
           Attestation

## Slide 22
Thank you