## Slide 1: Communication Manager

## Slide 2: Communication Manager

## Slide 3: Communication Manager
Uses the Proxy/Skeleton pattern
The CM provides the infrastructure that enables communication between Adaptive AUTOSAR Applications within one machine and with software entities on other machines, e.g. other Adaptive AUTOSAR applications or Classic AUTOSAR SWCs.
Supports for Dynamic Communication
Use of Service-oriented communication without dependency on a specific communication protocol
C++ interface compatible with C++14

## Slide 4: Service Oriented Architecture
Ara::com
Skeleton/Producer
SERVER APP
Proxy/Subscriber
CLIENT APP
SOME/IP
Offer Service
Find Service
Publishes Event/Field/vent
Subscribes
Event/Field/Methods

## Slide 6: Architecture
Language binding
POSIX-based OS
Communication/Network binding

## Slide 7: C++ Language Binding
  The language binding defines how the methods, events and fields of a service are used on API-level (C++/11)
  Type safe C++ interface
  Abstracts from Network binding details
  Polling- and event-driven programming styles are supported
  Zero-copy capability
  Supports safety (e.g. exception-free API subset, end-to-end protection support)
Adaptive Application
Language binding : ara::com
Network binding : E.g. SOME/IP(-SD)
Hardware / Virtual Machine / Container
POSIX-based Operating System

## Slide 8: C++ Language Binding: Proxy/Skeleton
Consumer: Adaptive Application
  The upper layer of the C++ Language Binding contains generated sources for the service interface described in the meta model
  A generator will generate C++ classes that contain type safe representations of the fields, events and methods of each respective service
  These C++ classes can be divided into Proxy and Skeleton classes:
    Proxy: Contains the consumer-side of the respective service interface
    Skeleton: Contains the provider-side of the respective service interface
  Adaptive Applications will use those generated classes to interact with ara::com
Meta Model (arxml)
MyServiceInterface
--- int my_field1
--- void my_func()
--- int my_func1()
--- my_event()
…
Generator
Proxy classes
Provider: Adaptive Application
Skeleton classes

## Slide 9: SOME/IP(-SD) Network binding
  Network binding defines how messages for service discovery, methods, events and fields are getting exchanged for:
    Intra-process communication: Process local
    Inter-process communication: E.g. POSIX-/QNX-/… IPC
    Inter-machine communication E.g. SOME/IP(-SD), DDS RTPS
  SOME/IP(-SD) consist of two specifications that are part of the Foundation (FO) documents:
    AUTOSAR_PRS_SOMEIPProtocol
    AUTOSAR_PRS_SOMEIPServiceDiscoveryProtocol
  SOME/IP(-SD) relies on using Ethernet and TCP/IP
  Middleware features:
    Serialization: Transforming into and from on-wire representation
    Service Discovery (SD): Dynamically find functionality
    RPC: Remote invocation of functions
    Publish/Subscribe: Dynamically configure which data is needed
    Segmentation of UDP messages: SOME/IP-TP
Adaptive Application
Language binding : ara::com
Network binding : SOME/IP(-SD)
Hardware / Virtual Machine / Container
POSIX-based Operating System

## Slide 11: References
https://www.autosar.org/fileadmin/user_upload/standards/adaptive/20-11/AUTOSAR_RS_CommunicationManagement.pdf
https://www.autosar.org/fileadmin/user_upload/standards/adaptive/20-11/AUTOSAR_SWS_CommunicationManagement.pdf
https://www.autosar.org/fileadmin/user_upload/standards/foundation/1-2/AUTOSAR_PRS_SOMEIPServiceDiscoveryProtocol.pdf

## Slide 12
Thank You